## Slide 1
Parallel Ranger Deck in Isaac Lab
Cyber Physical Systems Programming – Project
Students: Luca Samorì • Alexandru Zaporojanu • Tommaso Tieri
Teacher: Prof. Andrea Acquaviva | Supervisor: Dott. Sebastiano Mengozzi

## Slide 2
The Project
Extend the Isaac Lab sensors library with a custom ranger deck sensor tailored for navigation tasks.
Goal
Description
Create a custom software library to implement the Multi-Ranger Deck sensor within the Isaac Lab simulation environment, ensuring accurate environmental perception for drones.

## Slide 3
How it works: Multi-Ranger Deck
"The Crazyflie Multi-ranger deck gives the Crazyflie 2.X the ability to detect objects around it. This is done by measuring the distance to objects in the following 5 directions: front/back/left/right/up with mm precision up to 4 meters." [1]
5 Axes
Omnidirectional sensing
4 Meters
Maximum range
mm Precision
High accuracy
VL53L1x
5x ToF Sensors
Data Sheet Sensor:

## Slide 4
Mechanical: Weight: 2.3g | Size (WxHxD): 35x35x5mm.
Emitter: 940 nm invisible laser emitter (Class 1).
Receiver: SPAD (single photon avalanche diode) receiving array with integrated lens.
Field of View: 27° typical full field of view (FoV).
ROI: Programmable region of interest allows reduction of the sensor FoV. [2][3]





Sensor Specifications
Figure: 27° field of view (FoV) down to 15 [3]

## Slide 5
Basic Principle
Time of Flight – FlightSenseTM Principle
Basic Principle
It measures the time it takes for a photon to bounce back.
If the cone hits multiple objects at different distances, the histogram will show multiple peaks. The final measured distance is an average derived from these significant peaks [4]
In Practice
97% of the optical power in a cone of 27°.

## Slide 6
Physical Behavior vs Simulation Gap
One ray do not simulate the actual behavior of the sensor
We need to fill the Real-to-Sim Gap


Practical example: Generation of a map [5]
Expected map would approximate to red lines
In practice, we get an average when multiple
objects are present in the FoV

## Slide 7
The Real 2 Sim Gap:
Physical Behavior vs Simulation Gap
Rays distributed on the surface of 2 Concentric cones and 1 central ray receive distance measures.
The final output is a weighted average with higher weights given to central beams.
Rays number can be variated.
FoV can take whatever value, and cones will adapt (27°-15° is physical limit).
This physical choices are important for the code






## Slide 8
Code Structure
MultiMeshrRayCaster()
Base Class

Our code extends the base class; it’s the «brain» that customizes the sensor’s behavior

Benefits:​
Dynamic mesh detection​
Multimesh detection (cones, sphere, costume meshes ecc.)
Ease of usage​
GPU-Accelerated Parallelization.

Isaac Lab, using the MultiMeshRayCaster class, provides the infrastructure (ability to interact with meshes and compute everything in parallel on the GPU).

## Slide 9
How the 5 Cones Were Created
Defines the geometry for every sensor: 10 ray for each sensor (50 rays)
The algorithm automatically splits in 1 central ray, 1/3 inner rays and 2/3 outer rays.
Gets the 50 impact points from the GPU
Transforms the 50 points into 5 distances using a weighted average
Returns a Tensor (N, 5). A table where each row is a drone and the 5 columns are the distances in the 5 directions




ray_starts coordinate of the ray origin.

ray_dirs unit vector of the direction.

## Slide 10
Demo 1: Parallelization & Validation
Isaac Lab Parallelism
Test showing the operation of both the sensor measurement and the parallelization, a core feature of the Isaac Lab simulation environment.
Expected vs Measured
Comparison between theoretical distance (concrete walls) and the simulated ToF measurement.
Error Tracking
Error in millimeters plotted across all 5 directions (Front, Back, Left, Right, Down).

Accuracy of measurements
4 drone spawn with their respective sensors
Plotted the different measurements of all the sensors



## Slide 11
Demo 1: Results

## Slide 12
Demo 1: Results

## Slide 13
Stairs Environment
Demo 2: Flight Controller
Control Scheme Loop
Setpoint: Desired height (e.g., 0.5m)
Sensor (Multi-ranger Down): Reads actual altitude relative to the stairs.
Error: Setpoint - Sensor Reading.
PID Controller: Adjusts vertical thrust to minimize error.




The drone navigates over a set of stairs. We implemented a control loop to maintain a stable height.


## Slide 14
Demo 2: Results

## Slide 15
Mapping the Environment
As the drone moves through a corridor with rounded and sharp obstacles, the side lasers continuously gather point data.
Sensor Hits: Plotted as a point cloud on an X-Y plane.
Demonstrates the geometric fidelity of the sensor wrapping over complex shapes (like the semi-circular wall obstacle).


Demo 3: 2D Mapping

## Slide 16
Demo 3: 2D Mapping

## Slide 17
Conclusions and Future Works
 Add the functionality of being sensible to light sources since the real sensor has very bad performance outside were the amount of uv light coming from the sun is sensed as the vcsel emitter
 Sensible to surface colors

## Slide 18
Reference
Sources:
[1] Bitcraze AB Datasheet Multi-ranger deck - Rev 1
[2] STMicroelectronics, VL53L1X Datasheet: A new generation, long distance ranging Time-of-Flight sensor based on ST’s FlightSense™ technology
[3] AN5191, Application note, Using the programmable region of interest (ROI) with the VL53L1X
[4] AN5231, Application note, Cover window guidelines for the VL53L1X long-distance ranging Time-of-Flight sensor, Section 5.3
[5] Question about mapping using the VL53L1X sensor - Projects / General Guidance - Arduino Forum